## Slide 1: Probabilistic Profiling of Stateful Data Planes for Adversarial Testing
Qiao Kang Jiarong Xing Yiming Qiu Ang Chen
Main contributors

## Slide 2
Background: Programmable data planes
Programmable switches and NICs are on the rise
  Controlled in high-level languages (e.g., P4)
  Customized protocols (e.g., user-defined headers)
  Programmable match/actions (e.g., add/rm/mod headers)
  Stateful packet processing (e.g., using SRAM-based registers)
Memory
ALU
Match/
Action
Table
Match/
Action
Table
Match/
Action
Table
Programmable
Parser
Programmable
Deparser
Switch control plane
PCIe bus
Stages
Stages

## Slide 3
Background: Data plane systems
Programmable data planes as an offloading platform
  Network monitoring (e.g., Blink-NSDI’19..)
  Network security (e.g., NetWarden-USENIXSec’20)
  Network applications (e.g., NetCache-NSDI’18), …
  Data plane systems: far more complex than forwarding programs
Offloaded ”apps”
Programmable switches

## Slide 4
Example: Detecting remote link failures
Blink (NSDI 2019)
  Goal: Infer remote link failures based on TCP retransmission
  Monitors per-flow retransmission based on TCP SEQ
  Uses sliding window to count retransmitting flows
  Activates backup path if exceeds a threshold
Flow tuples | Status
10.0.0.5:22 | Normal
10.0.0.8:22 | Retrans
Flow monitoring
Failure inference
Rerouting upon failure
Num. of retrans. flows
Path | Status
0 (primary) | Down
1 (backup) | Up
Routing table for 10.0.0.0/8
+1
> X?
Packet
in
Per-flow table for 10.0.0.0/8
Packet
out

## Slide 5
Is this always “safe”?
Blink assumptions about network traffic:
  Normally, packets don’t need to be retransmitted
  Concurrent retransmissions at scale are rare
  But such traffic patterns can be “crafted”!
“Adversarial” traces may cause chaotic routing
Data plane systems

## Slide 6
Motivation: Probabilistic profiling
Many data plane systems have stochastic behaviors
Goal: Probabilistic profiling of data plane systems
  Application: Adversarial testing
  Also: Hotspot identification, profile-guided optimization, ..
P4 program
......
If (cond)
foo ()
Else
bar ()
......
If(cond)
bar()
﻿Control.ingress:
foo()
Else
normal
retrans
Data plane systems
Program analysis
Probabilistic profile
foo
bar
Chart: 
| EC 1 | EC 2
 | 0.9 | 0.1
Chart: 
| EC 1 | EC 2
 | 0.1 | 0.9
foo
bar
Expected
distribution
Adversarial
distribution

## Slide 7
Data plane systems are on the rise
Motivation: Probabilistic profiling for adversarial testing
The P4wn profiler
  Starting point: Symbolic execution
  Characterizing probabilities
  Handling stateful data structures
  Analyzing deep loops
Evaluation
Summary
Outline

## Slide 8
Starting point: Symbolic execution
Goal: Enumerate program behaviors and generate inputs for each behavior
  Create symbolic inputs and collect symbolic constraints
  Fork execution paths for branch and loop conditions
  Invoke solver to compute satisfying assignments
packet_handler (pkt) {
pkt.ttl --;
if (pkt.ttl > 0) {
forward packet
} else {
drop packet
}
}
ttl=10
ttl=9
ttl=9
Concrete/normal
execution
Symbolic
execution
ttl=x
ttl=x-1
x-1>0
x-1<=0
SMT solver

## Slide 9
Symbolic execution is not enough
Data plane system profiling presents unique challenges
  Computing probabilities
  Handling approximate data structures
  Analyzing stateful loops
If(cond)
bar()
﻿Control.ingress:
foo()
Else
normal
retrans
Computing probabilities
Hash tables, sketches, bloom filters
+1
+1
+1
packet_handler (pkt) {
pkt_cnt ++;
if (pkt_cnt == 1M) {
//sample packet
}
Stateful loops
Loop
body

## Slide 10
From executions to probabilities
Approach: Count the # of satisfying solutions
  All possible header values form a “headerspace”
  Program executions produce subspaces
  Prob = Volume(subspace)/Volume(headerspace)
Model counting solvers, or by querying network traces
The entire header space
Other traffic
Retransmissions
Normal trans
TCP traffic
Behavior 3
Behavior 4

## Slide 11
Handling approximate data structures
Examples: Hash tables, sketches, bloom filters
  Very common building blocks in data plane systems
State-of-the-art technique: Symbolic arrays
  A symbolic access may fall on any array locations
  Create execution paths to capture uncertainty
  Doesn’t scale with array size; sketches: O(10k) elements
Modeling a hash table as a symbolic array
?
?
?
A[x].insert(v1);
…
A[x].insert(v2);
…
A[x].insert(v3);
CRC(flowkey)

## Slide 12
Solution: Greybox analysis
Approach: Use statistical properties of the approximate data structures to model abstract behaviors
  Keep “probabilistic” state distribution instead of actual state
  Scales independently of the array size
Pr(Col) = ColRate(k,N)
Pr(Hit) = HitRate(k,N)
[ (v1, p1), (v2, p2)]
Size = k, max = N
[ (v1, p1), (v2, p2), (v3, p3)]
Size = k + 1, max = N
[ (v1, a1), (v2, a2), (v3, a3)]
Size = k, max = N
[ (v1, q1), (v2, q2), (v3, q3)]
Size = k, max = N
Modeling a ‘insert(v3)’ operation
p1 = (p1 * k) / (k + 1)
p2 = (p2 * k) / (k + 1)
p3 = 1 / (k + 1)
Pr(Empty) = (N-k) / N

## Slide 13
Handling stateful loops
P4 programs are executed in an “implicit” loop
  Every packet triggers the loop execution once
  One execution impacts the next via stateful variables
  Naïve solution needs a long sequence of symbolic packets
    K branches, t packets: O(K^t) execution paths
packet_handler (pkt) {
//identify TCP pkts
tcp_pkt_cnt ++;
if (tcp_pkt_cnt == 1M) {
//sample packet
}
Stateful loops
Loop
body
Path constraints
…
p1.proto=6
p1.proto!=6
p2.proto=6
!=6
!=6
=6
p3.proto=6
…

## Slide 14
Solution: Telescoping
Path constraints
…
p1.proto=6
p1.proto!=6
p2.proto=6
!=6
!=6
=6
p3.proto=6
…
Observation: Periodic loop behaviors are common in P4 programs due to event monitors
  Use a short symbolic packet sequence as probe
  Analyze which execution paths lead to monitor increments
  Stretch/repeat the short sequence into a longer one
  Compute probabilities based on stretched sequence

## Slide 15
Evaluation setup
P4wn prototype:
  6500 LoC of C
  Extends the KLEE symbolic execution engine
A range of programs
  Traditional forwarding programs (stateless)
  Data plane systems (stateful)
    Blink, NetWarden, NetCache, …
Baseline: KLEE

## Slide 16
Microbenchmarks: Greybox analysis
P4wn scales independently of data structure size
Figure for CMS; other results in paper

## Slide 17
Microbenchmarks: Telescoping
P4wn uses 4 symbolic packets for telescoping
Figure for Blink; other results in paper

## Slide 18
Probabilistic profiles + adversarial testing
Method: Rank code blocks by probability, and generate test traces to lowest ones
P4wn detected all known adversarial traces in the tested systems
Adversarial traces caused significant disruption
System | Description | Adversarial trace(s)
Blink [NSDI’19] | Link failure detector | Concurrent TCP retrans.
NetCache [SOSP’17] | Key/value cache | Changing “hot” keys
*Flow [ATC’18] | Network telemetry | Frequent collision
P40f [CoNEXT’19] | OS fingerprinting | Signature mismatch
NetHCF [ICNP’19] | Spoofed traffic filtering | Frequent unseen IPs
Poise [Sec’20] | Access control | Hash collisions (+)
NetWarden [Sec’20] | Covert channel defense | Timing modulation (+)

## Slide 19
Probabilistic profiles + adversarial testing (Cont’d)
A subset of code blocks ranked by probabilities
  Red: produces disruptive traces
  Green: non-disruptive traces
Corner-cases (often) lead to disruptive behaviors

## Slide 20
Summary
Motivation: Probabilistic profiling of data plane systems
  Application: Adversarial testing
    Identify all possible behaviors and their probabilities
    Generate adversarial traces for system testing
  The P4wn system
    Computes probabilities using model counting
    Handles stateful data structures via greybox analysis
    Analyzes deep loops using telescoping
  Evaluation
    Scales to complex programs
    Generates effective testing traces
  Thank you!