## Slide 1: Secure State Migration in the Data Plane
Jiarong Xing, Ang Chen, T.S. Eugene Ng
Rice University

## Slide 2
The network is becoming programmable
Programmable data planes (PDPs)
  Can be programmed in high-level languages (e.g., P4)
  Support customized protocols and match/actions, persistent state
  Run at linespeed (Tbps)
Memory
ALU
Match/
Action
Table
Match/
Action
Table
Match/
Action
Table
Switch control plane
PCIe bus
Stages
Stages

## Slide 3
Distributed PDP systems
Distributed systems require state synchronization
  Hula: Link utilization  Least utilized paths
  Contra: Policy defined metrics  Best routes
  FastFlex: Suspicious IPs  Drop or reroute traffic
Load balancers
  Hula-SOSR’16
Link-flooding defenses
  FastFlex-HotNets’19
Performance-aware routing
  Contra-NSDI’20

## Slide 4
Problem: Secure state synchronization
Copy data from the source to the destination periodically
Data can be in different shapes
The network is untrusted
untrusted
Source
Destination

## Slide 5
Three key goals
Completeness
Copying data from the source to the destination completely.
Low overhead
Do not utilize too much switch memory and link bandwidth.
Integrity guarantee
The data cannot be modified or spoofed by attackers.

## Slide 6
State of the art: Swing State (SOSR’17)
Completeness: Depends on normal traffic pattern
Overhead: Has high traffic overhead.
Integrity: No integrity guarantee.
Normal traffic
Register array
Clone
Migration destination
Normal destination

## Slide 7
Can we design a data plane synchronization protocol that satisfies all three goals?
P4Sync

## Slide 8
Data plane protocol
Runs in the data plane with minimal local control plane involvement
Completeness
Scans and copies the register array end to end
Low overhead
Integrity guarantee
Caches and aggregates dirty data in a delta array
Per-packet MAC and periodic RSA signatures
P4Sync overview
P4Sync

## Slide 9
Outline
Motivation: Data plane state synchronization
State of the art: Cannot satisfy all three goals
Approach: P4Sync
P4Sync design
  Challenge #1: Achieving completeness with low overhead
  Challenge #2: Data integrity guarantee
Evaluation
Conclusion

## Slide 10
      Solution:
        Scanning register arrays end to end
        Caching and aggregating new updates in a delta array
Challenge #1: Achieving completeness with low overhead
Scanning register arrays
Caching new updates

## Slide 11
Scanning register arrays end to end
Using the traffic generator in programmable switches
Controlling the synchronization to a reasonable rate
Maintaining a progress index
Migration destination
Traffic generator
0
1
2
3
4
…
98
100
Rate control
Scanning direction
Register array

## Slide 12
Caching and aggregating dirty data in a delta array
Caching and aggregating dirty data in a delta array
Scanning through the delta array at the end
Normal traffic
Register array
Migration destination
Traffic generator
0
1
2
3
4
…
98
100
Rate control
Delta array
0
1
2
3
4
…
98
100

## Slide 13
      Naïve Solution: Signing every packet with RSA.
        In the data plane: Only support limited arithmetic operations
        In the control plane: Cannot handle Tbps traffic.
      Our solution: Amortizing overhead over a set of packets
        Inspired by stream authentication: EMSS (S&P’00)
Challenge #2: Data integrity guarantee
Limited arithmetic operations
Software speed

## Slide 14
Amortizing overhead over a set of packets
      Building a hash chain in the data plane.
      Signing packets in batch in the control plane.
      How to handle packet loss and reordering?
116
115
114
113
…
117
112
111
hash(i) = hash(PH, hash(i − 1))
Packet header fields
Hash of last packet
Hash of this packet
MAC
MAC
MAC
MAC
MAC
MAC
MAC
RSA
RSA

## Slide 15
Outline
Motivation: Data plane state synchronization
State of the art: Cannot satisfy all three goals
Approach: P4Sync
P4Sync design
  Challenge #1: Achieving completeness with low overhead
  Challenge #2: Data integrity guarantee
Evaluation
Conclusion

## Slide 16
Experimental setup
Proof-of-concept prototype:
  Runs in Mininet + P4 bmv2.
  Measured RSA speed in a Wedge 100BF-32X Tofino switch
Scenario:
  A source switch transmits a hash array to a destination switch.
  The attacker in the middle tries to modify the data.
Baseline:
  Swing State (SOSR’17)

## Slide 17
How much traffic overhead does P4Sync incur?
Swing State achieves 100% completeness when overhead is 8.
P4Sync achieves 100% completeness when overhead is 2.
P4Sync can transmit data completely with low traffic overhead.
17

## Slide 18
How well can P4Sync defend against integrity attacks?
18
trusted
trusted
Source
Destination
P4Sync can always detect the packet modification.
RSA-2048: 2.15ms for signature; 0.07ms for verification.
P4Sync can defend against integrity attacks effectively and efficiently!

## Slide 19
Outline
Motivation: Data plane state synchronization
State of the art: Cannot satisfy all three goals
Approach: P4Sync
P4Sync design
  Challenge #1: Achieving completeness with low overhead
  Challenge #2: Data integrity guarantee
Evaluation
Conclusion

## Slide 20
Data plane protocol
Runs in the data plane with minimal local control plane involvement
Completeness
Scans and copies the register array end to end
Low overhead
Integrity guarantee
Caches and aggregates dirty data in a delta array
Per-packet MAC and periodic RSA signatures
P4Sync overview
P4Sync

## Slide 21
Conclusion
Motivation: Data plane state synchronization
Three key goals:
  Completeness
  Low overhead
  Integrity guarantee
Our approach: P4Sync
  Scans and copies the register array end to end
  Caches and aggregates dirty data in a delta array
  Per-packet MAC and periodic RSA signatures
Source code: https://github.com/jiarong0907/P4Sync
Looking for internship in 2021 summer!
Questions?
21